## Slide 1
第一讲 CPU的基本功能和基本组成
第二讲 单周期MIPS处理器的设计
第三讲 微程序控制原理与异常处理
第5章 中央处理器：数据通路和控制器
Notes: Start X:40

## Slide 2: 第一讲 CPU的基本功能和基本组成
CPU的功能及其与计算机性能的关系
指令的四个基本功能
数据通路的基本结构
  常用的操作元件
  常用的状态元件：寄存器组与存储器
数据通路的时序控制
总线结构数据通路中四种基本功能的实现
主 要 内 容

## Slide 3: CPU功能及其与计算机性能的关系
CPU执行指令的过程（回顾）
    取指令
    PC+“1”送PC
    指令译码
    进行主存地址运算
    取操作数
    进行算术 / 逻辑运算
    存结果
    以上每步都需检测有无“异常”，若有则
    自动切换到异常处理程序
    检测是否有“中断”请求，有则转中断处理
CPU的实现与计算机性能的关系
  计算机性能(程序执行时间)由三个关键因素决定（回顾）:
    指令数目、CPI、时钟周期
    指令数目由编译器和ISA决定
    时钟周期和CPI由CPU的实现以及其他因素来决定
因此，CPU的设计与实现非常重要！它直接影响计算机的性能。
指令执行过程
取指阶段
译码和
执行阶段

## Slide 4: 组成指令功能的四种基本操作
每一条指令的功能都是由以下四种基本操作的组合来实现：
  读取某一主存单元的内容，并将其装入某个寄存器（取指， 取数）
  把一个数据从某个寄存器存入给定的主存单元中（存结果）
  把一个数据从某个寄存器送到另一个寄存器或者ALU（取数，存结果）
  执行算术或逻辑运算（PC+1，计算地址，运算）
操作功能的形式化描述
  描述语言称为寄存器传送语言RTL (Register Transfer Language)
  本章所用的RTL规定如下：
    （1）用R[r]表示寄存器r的内容；
    （2）用M[addr]表示主存单元addr的内容；
    （3）传送方向用“←”表示，传送源在右，传送目的在左；
    （4）对于程序计数器PC，直接用PC表示其内容。
    例如，R[$8] ← M[R[$9]+4]的含义是：
    将寄存器$9的内容加4得到的内存地址单元的内容送寄存器$8中。

## Slide 5: CPU基本组成原理图
执行部件
控制部件
CPU 由 执行部件 和 控制部件组成
控制部件 主要由 指令译码器 和 控制信号形成部件 组成
指令寄存器----IR
程序计数器---PC
执行部件 主要由ALU、 通用寄存器和状态寄存器 组成

## Slide 6: 数据通路在计算机组成结构中的位置
计算机的五大组成部分：
什么是数据通路（DataPath）?
  指令执行过程中，数据所经过的路径，以及路径上的部件。包括ALU、通用寄存器、状态寄存器、MMU、cache、中断处理逻辑等
  数据通路中专门进行数据运算的部件称为执行部件或功能部件。
控制器（Control）的功能
  对指令进行译码，生成指令对应的控制信号，控制数据通路的动作。它向执行部件发出控制信号，是指令的控制部件。
Control
Memory
CPU
Input
Output
Datapath
Datapath
Notes: Before we go any further, let’s step back for a second and take a look at the big picture.
All computer consist of five components: (1) Input and (2) output devices. (3) The Memory System. And the (4) Control and (5) Datapath of the Processor.
Today’s lecture covers the datapath design.
In the next lecture, I will show you how to design the processor’s control unit.
+1 = 5 min. (X:45)

## Slide 7: 数据通路的基本结构
数据通路由两类元件组成
  组合逻辑元件（也称操作元件）
  时序逻辑元件（也称状态元件，或存储元件）
元件间的连接方式有两种方式
  总线连接方式
  分散连接方式
数据通路如何构成？
  由“操作元件”和“存储元件”通过总线方式或分散方式连接而成
数据通路的功能是什么？
  进行数据传送、处理和存储
数据通路完整的定义是：
由操作元件和存储元件通过总线方式或分散方式连接而成的进行数据传送、处理和存储的路径。
搬数据
数据运算
存数据
数据通路功能示意图

## Slide 8: 常用的操作元件（组合逻辑元件）
加法器(Adder)
多路选择器 (MUX)
算逻部件(ALU)
32
A
B
32
Y
32
Select
MUX
32
32
A
B
32
Result
ZF,CF,OF…
ALUctr
ALU
32
32
A
B
32
Sum
Carry
Adder
CarryIn
3
Decoder
out0
out1
out7
out2
译码器(Decoder)
何时要用到adder, ALU, MUX or Decoder?
控制信号
组合逻辑元件的特点：
其输出只取决于当前的输入。即：若输入一样，则其输出也一样
无定时：所有输入到达后，经过一定的逻辑门延时，输出端改变，并保持到下次改变，不需要时钟信号来定时
加法器需要什么控制信号?
Back
Notes: Based on the Register Transfer Language examples we have so far, we know we will need the following combinational logic elements.
We will need an adder to update the program counter.
A MUX to select the results.
And finally, an ALU to do various arithmetic and logic operation.
+1 = 30 min. (Y:10)

## Slide 9: 状态元件：时序逻辑电路
状态元件（存储元件）的特点：
  具有存储功能，在时钟控制下输入被写到电路中，直到下个时钟到达
  输入端状态由时钟决定何时被写入，输出端状态随时可以读出
定时方式：规定信号何时写入状态元件
  边沿触发（edge-triggered）方式：
    状态单元中的值只在时钟边沿改变。每个时钟周期改变一次。
      上升沿（rising edge） 触发：在时钟正跳变时进行读/写。
      下降沿（falling edge）触发：在时钟负跳变时进行读/写。
最简单的状态单元（回顾：数字逻辑电路课程内容）：
  D触发器：一个时钟输入、一个状态输入、一个状态输出
cycle time
rising edge
falling edge

## Slide 10: 存储元件中何时状态被改变？
切记：状态单元的输入信息总是在一个时钟的有效边沿到达后的“Clk-to-Q”时才被写入到单元中，此时的输出才反映新的状态值
数据通路中的存储元件有两种：寄存器(组) 和 存储器
Q总是在clock-to-Q后跟着D变化
这期间D的变化不影响Q
0
0
1
1
( Latch Prop - 锁存延迟 )
输入
输出
Clk

## Slide 11: 存储元件: 寄存器和寄存器组
寄存器（Register）
  有一个写使能（Write Enable-WE）信号
  WE=0: 时钟边沿到来时，输出不变
  WE=1: 时钟边沿到来时，输出变为输入
  若每个时钟边沿都写入，则不需WE信号
寄存器组（Register File）：包含32个寄存器
  两个读口(组合逻辑操作)：busA和busB分别由RA和RB选择32个寄存器之一输出。地址RA或RB有效后，经一个“取数时间(AccessTime)”，busA和busB有效。
  一个写口（时序逻辑操作）：写使能为1的情况下，时钟边沿到来时，busW上的值开始被写入RW指定的寄存器中。
Clk
Data In
Write Enable
N
N
Data Out
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 32-bit
Registers
Back
Notes: As far as storage elements are concerned, we will need a N-bit register that is similar to the D flip-flop I showed you in class.
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is zero.
The content is updated at the clock tick ONLY if the Write Enable signal is set to 1.
+1 = 31 min. (Y:11)
Complement:
To know more detailed diagram for a register, see page B22-B25.

## Slide 12
寄存器组的内部结构
busW
C
D
0
31
M
U
X
M
X
U
Register 0
Register 1
Register 30
Register 31
Write Enable
RW
32-to-1
Decoder
RA
RB
busA
busB
Clk
C
D
C
D
C
D
每个寄存器由32个触发器组成;
输入数据来自busW，读出数据分别送busA和busB;
WriteEnable信号控制是否写入新值。
Back to add
32
5
32
32
5
5
32
32
32
32
32
32
32
32
32
32
32
32

## Slide 13: 存储元件: 理想存储器
理想存储器（ idealized memory ）
  Data Out：32位读出数据
  Data In： 32位写入数据
  Address：读写共用一个32位地址
  读操作（组合逻辑操作）：
    地址Address有效后，经一个“取数时间AccessTime”，Data Out上数据有效。
  写操作（时序逻辑操作） ：
    写使能为1的情况下，时钟Clk有效边沿到来时，Data In传来的值开始被写入Address指定的存储单元中。
Clk
Data In
Write Enable
32
32
DataOut
Address
为简化数据通路操作说明，把存储器简化为带时钟信号Clk的理想模型。
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (DataIn) and one output bus (DataOut).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.
+2 = 35 min. (Y:15)

## Slide 14: 数据通路与时序控制
同步系统(Synchronous system)
  所有动作有专门时序信号来定时
  由时序信号规定何时发出什么动作
  例如，指令执行过程每一步都有控制信号控制，由定时信号确定控制信号何时发出、作用时间多长
什么是时序信号？
  同步系统中用于进行同步控制的定时信号，如时钟信号
什么叫指令周期？
  读取并执行一条指令的时间
  每条指令的指令周期都一样吗？
早期计算机的三级时序系统
  机器周期 - 节拍 - 脉冲
  指令周期可分为取指令、读操作数、执行并写结果等多个基本工作周期，称为机器周期。
  机器周期有取指令、存储器读、存储器写、中断响应等不同类型的机器周期。

## Slide 15: 数据通路与时序控制 ---早期计算机的三级时序
现代计算机已不再采用三级时序系统，机器周期的概念已逐渐消失。
整个数据通路中的定时信号就是时钟，一个时钟周期就是一个节拍。

## Slide 16: 数据通路与时序控制 ---现代计算机的时钟周期
假定采用下降沿触发（负跳变）方式（也可以是上升沿方式）
  所有状态单元在下降沿写入信息，经过锁存延时(Latch Prop ) 后输出有效
  时钟周期= Latch Prop + Longest Delay Path + Setup + Clock Skew(时钟偏移)
约束条件：(Latch Prop + Shortest Delay Path - Clock Skew) > Hold Time
Clk
寄存器的输入可变化
Setup
Hold
.
.
.
.
.
.
.
.
.
.
.
.
Setup
Hold
数据通路由 “ … + 状态元件 + 操作元件( 组合电路) + 状态元件 + …” 组成
只有状态元件能存储信息，所有操作元件都从状态元件接收输入，并将输出写入状态元件中。
操作元件的输入为前一时钟状态元件生成的数据，输出为当前时钟状态元件所用的数据。
Clk
Clk
即：操作元件输出有效信号最快的也必须在下一级状态元件的输入保持时间之后出现。
Notes: Remember, we will be using a clocking methodology where all storage elements are clocked by the same clock edge.
Consequently, our cycle time will be the sum of:
(a) The Clock-to-Q ( or latch propagation) time of the input registers.
(b) The longest delay path through the combinational logic block.
(c) The set up time of the output register.
(d) And finally the clock skew.
In order to avoid hold time violation, you have to make sure this inequality is fulfilled.
+2 = 18 min. (X:58)
Complements:
Why use edge-triggerd clocking methodology? simpler to explain in contrast to level-triggered.
Clock skew: difference in absolute time between the times when two state elements see a clock edge. It arises because the clock signal often follows different paths, with slightly delays, to reach two different state elements. Clock skew may cause a forward race of new inputs to the next flip-flop, leading to incorrect operation. (see Fig.B.31 at page B-41).
Clock-to-Q(or latch propagation): the propagation time of signal through a flip-flop from clock to the output Q. That is why it is called clock to Q time.
Setup time/hold time of flip-flop: the minimum time during which the input must be valid( or stable) before/after the clock edge.(page B-24)
(Latch Prop + Shortest Delay Path - Clock Skew) > Hold Time : this might be difficult to explain, but otherwise it will cause the race problem as shown in Fig.B.31.

## Slide 17: 单总线数据通路
四种基本操作的时序
  在寄存器之间传送数据
    R0out，Yin
  完成算术、逻辑运算
    R1out，Yin
    R2out，Add，Zin
    Zout，R3in
  从主存取字
    R1out，MARin
    Read, WMFC (等待MFC)
    MDRout，R2in
  写字到主存
    R1out，MARin
    R2out，MDRin，
    Write, WMFC
R[R2]←M[R[R1]]
M[R[R1]] ← R[R2]
CPU访存有两种通信方式
早期：直接访问MM, “异步”方式，用MFC（存储器完成）信号进行应答。
现在：先Cache后MM，“同步”方式，无需应答信号。
问题：时钟周期的宽度如何确定？
以“Riout,OP,Zin”所花时间来确定还是以 “Read/Write”所花时间来确定？ 以上四种操作各需要几个时钟周期？
1Cycle?
3Cycles?
3Cycles?
3Cycles?
Read/Write时间更长，故以此为准！
OP: Add、Sub、And、Or 等
通用寄存器
总线连接方式！
内总线
外总线
R[R3]←R[R1]+R[R2]
Y←R[R0]
寄存器与总线的连接
Notes: WMFC：Wait Memory Function Completed

## Slide 18: 三总线数据通路
单总线中一个时钟内只允许传一个数据，因而指令执行效率很低
可采用多总线方式，同时在多个总线上传送不同数据，提高效率
例如：三总线数据通路
  总线A、B分别传送两个源操作数，总线C传送结果
  单总线中的暂存器Y和Z在此可取消，Why？
  采用双口通用寄存器组
  如何实现： R[R3] ←R[R1] op R[R2]
    R1outA，R2outB，op，R3inC
    只要一个时钟周期（节拍）即可！
目前大都采用流水线方式执行指令，单总线或三总线的总线式数据通路很难实现指令流水执行。
Z
Y
下面以MIPS指令系统为例介绍非总线式CPU的设计。
三个总线各自传不同数据，不会发生冲突，故无需Y和Z
通用寄存器组

## Slide 19
第一讲小结
CPU设计直接决定了时钟周期宽度和CPI，所以对计算机性能非常重要！
CPU主要由数据通路和控制器组成
  数据通路：实现指令集中所有指令的操作功能
  控制器：控制数据通路中各部件进行正确操作
数据通路中包含两种元件
  操作元件（组合电路）：ALU、MUX、Ext.、Adder、Reg/Mem Read等
  状态 / 存储元件（时序电路）：PC、Reg/Mem Write
数据通路的定时
  数据通路中的操作元件没有存储功能，其操作结果必须写到存储元件中
  在时钟到达后经过clk-to-Q时间存储元件开始更新状态

## Slide 20
第二讲 单周期MIPS处理器的设计
主 要 内 容
基于一个MIPS指令子集的数据通路设计
  下条指令地址计算与取指令部件
  设计各类指令的数据通路
  综合所有指令的数据通路
单周期控制器的设计
  公共操作：取指令和计算下址PC
  考察每条指令在数据通路中的执行过程和涉及到的控制信号的取值
  汇总各指令的控制信号取值
  分析ALU操作对应的控制信号与func字段之间的关系
  设计ALU局部控制单元
  设计主控制单元

## Slide 21
加法与减法
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
这些指令具有代表性！
有算术运算、逻辑运算；有RR型、RI型；有访存指令；有条件转移、无条件转移。
本讲目标：实现以上7条指令对应的数据通路！
教材中实现了11条指令，可将7条指令和11条指令的数据通路进行对比，以深入理解设计原理。
大家记得是哪三种类型？
R-Type、I-Type、J-Type
复习：MIPS的三种指令类型
R-Type
I-Type
J-Type
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 22: 设计处理器的步骤
第一步：分析每条指令的功能，并用RTL(Register Transfer Language)
来表示。
第二步：根据指令的功能给出所需的元件，并考虑如何将他们互连。
第三步：确定每个元件所需控制信号的取值。
第四步：汇总所有指令所涉及到的控制信号，生成一张反映指令与控制信 号之间关系的表。
第五步：根据表得到每个控制信号的逻辑表达式，据此设计控制器电路。
处理器设计涉及到数据通路的设计和控制器的设计
数据通路中有两种元件
  操作元件：由组合逻辑电路实现
  存储（状态）元件：由时序逻辑电路实现
ISA确定后，进行处理器设计的大致步骤如下：
Notes: So let’s design a processor. How and where do we start?
Well, the best place to start is the processor’s instruction set architecture. After all, the goal of your design is to execute the instructions in the instruction set correctly.
What you need to do is to describe each instruction’s operation in register transfer language.
By looking at the Register Transfer Language description of the instruction, you can figure out the datapath components you need and how to connect these components together.
As I will show you, each datapath component will have its own set of control signals.
And the last step of the processor design task is to design the control unit that generates the control signals for the datapath.
So what do we mean by Register Transfer Language?
+2 = 27 min. (Y:07)

## Slide 23: 取指令公共操作及其部件(Instruction Fetch Unit)
每条指令都有的公共操作：
  取指令： M[PC]
  更新PC：PC ← PC + 4
  转移（Branch and Jump）时，PC内容要再次被更新为 “转移目标地址”
两个操作的顺序：先取指令，再改PC的值（具体实现时，可以并行）
绝不能先改PC的值，再取指令
下地址逻辑：形成新的PC
取指后，各指令功能不同，数据通路中信息流动过程也不同
下面分别对每条指令进行相应数据通路的设计
32
Instruction Word
Address
Instruction
Memory
PC
Clk
Next Addr
Logic
取指令部件
Notes: Now let’s take a look at the first major component of the datapath: the instruction fetch unit.
The common RTL operations for all instructions are:
(a) Fetch the instruction using the Program Counter (PC) at the beginning of an
instruction’s execution (PC -> Instruction Memory -> Instruction Word).
(b) Then at the end of the instruction’s execution, you need to update the
Program Counter (PC -> Next Address Logic -> PC).
More specifically, you need to increment the PC by 4 if you are executing sequential code.
For Branch and Jump instructions, you need to update the program counter to “something else” other than plus 4.
I will show you what is inside this Next Address Logic block when we talked about the Branch and Jump instructions.
For now, let’s focus our attention to the Add and Subtract instructions.
+2 = 37 min. (Y:17)

## Slide 24: 加法和减法指令(R-type类型）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
首先考虑add和sub指令（R-Type指令的代表）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 25: 加法指令add的RTL描述
add rd, rs, rt
  M[PC]
  R[rd] ← R[rs] + R[rt]
  PC ← PC + 4
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
从rs、rt 所指的寄存器中取数后相加。
若结果不溢出，则将结果送rd 所指的寄存器中；
若结果溢出，则不送结果，并转到“溢出处理程序”执行。
从PC所指的内存单元中取指令
PC加4，使PC指向下一条指令
Notes: Here is an example. In terms of Register Transfer Language, this is what the Add instruction need to do.
First, you need to fetch the instruction from memory.
Then you perform the actual add operation.
And finally, you need to update the program counter to point to the next instruction.
+1 = 28 min. (Y:08)

## Slide 26: RR（R-type）型指令的数据通路
功能：R[rd] ← R[rs] op R[rt]，如：add rd, rs, rt
不考虑公共操作，仅R-Type指令执行阶段的数据通路如下：
ALUctr,RegWr: 指令译码后产生的控制信号
Ra, Rb, Rw 分别连接指令的rs, rt, rd
“add rd, rs, rt”控制信号有哪些？取值=？
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
溢出时，不写结果并需转异常处理程序
寄存器组结构
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rd
ALU
溢出
Write Enable
ALUctr=add，RegWr=1
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file’s Ra, Rb, and Rw input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
But setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus’s Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
+3 = 42 min. (Y:22)

## Slide 27: 带立即数的逻辑指令（ori指令）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
作为I-Type指令和逻辑运算指令的代表
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 28: 带立即数的逻辑指令ori的RTL描述
ori rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  R[rt] ← R[rs] or ZeroExt(imm16)
  立即数零扩展，并与rs内容做“或”运算
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
imm16
0
16
15
31
16 bits
16 bits
0000 0000 0000 0000
零扩展 ZeroExt(imm16)
思考：应在前面数据通路上加哪些元件和连线？用何控制信号？
逻辑运算，立即数为逻辑数
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: The or immediate is a I-type instruction.
The immediate field of the instruction (Imm16 of the format diagram) is zero extended to 32 bits before it is operated with the other operand.
The other operand is selected by the Rs field of the instruction.
The destination register of this instruction will be selected by the Rt field.
+2 = 57 min. (Y:27)

## Slide 29: 带立即数的逻辑指令的数据通路
R[rt] ← R[rs] or ZeroExt[imm16]] Example: ori rt, rs, imm16
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
Don’t Care rt
ALU
R-Type类型的结果写入rd，ori指令是写入rt
R-Type的操作数来自busB
应增加兰色部分，为什么？
Ori指令的控制信号：RegDst=？；RegWr=？；ALUctr=？；ALUSrc=？
rt
rd
RegDst
Mux
0
1
Ext
Mux
16
32
imm16
ALUSrc
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
1
1
1
or
溢出
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 30
访存指令中的数据装入指令 (lw指令)
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
3. 考虑lw 指令（访存指令的代表）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits

## Slide 31
Lw指令的RTL描述
lw rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Addr ← R[rs] + SignExt(imm16) 计算存储单元地址 (立即数符号扩展！)
  R[rt] ← M [Addr] 装入数据到寄存器rt中
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
immediate
0
16
15
31
16 bits
16 bits
0000 0000 00000 0000
0
0
16
15
31
immediate
16 bits
16 bits
1111 1111 1111 1111
1
符号扩展( 为什么不是零扩展? ) ：
思考：应在原数据通路上加哪些元件和连线？用何控制信号？
立即数用补码表示
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 32: 装入(lw)指令的数据通路
R[rt] ← M[ R[rs] + SignExt[imm16] ] lw rt, rs, imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
Don’t Care
(rt)
rd
RegDst
Mux
Mux
32
16
imm16
ALUSrc
ALU
加兰色部分。为什么？
控制信号： RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemtoReg
0
1
Ext
ExtOp
Mux
MemtoReg
Addr
Data
Memory
32
0
1
0:零扩展，1：符号扩展
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
1
1
1
1
1
addu
addu:不影响溢出标志
溢出
各取何值？
Notes: ALU控制信号addu与add区别：add加法结果要判断溢出，addu结果不判溢出。
Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 33: 访存指令中的存数指令 (sw)
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
4. 考虑sw 指令（访存指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 34: 存数指令sw的RTL描述
sw rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Addr ← R[rs] + SignExt(imm16) 计算存储单元地址（符号扩展！）
  Mem[Addr] ← R[rt] 寄存器rt中的内容存到内存单元中
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
思考：应在原数据通路上加哪些元件和连线？用何控制信号？
Notes: Just like the load instruction:
(a) The store instruction also uses the I format.
(b) And the store instruction also forms the memory address by adding the contents
of the register selected by the Rs field to the sign extended immediate field.
However, unlike the load instruction, which gets data from memory and put the data into the the register file, the store instruction:
(a) Get the register selected by the Rt field of the instruction (R[rt]).
(b) And then write this register into the data memory.
+2 = 62 min. (Y:42)

## Slide 35: 存数(sw)指令的数据通路
M[ R[rs] + SignExt[imm16] ← R[rt] ] Example: sw rt, rs, imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Addr
Data
Memory
32
MemWr
ALU
0
1
0
1
加兰色部分。为什么？
控制信号RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg 各取何值？
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
x
0
addu
1
1
1
x
溢出
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the exact same way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 36: 分支（条件转移）指令（相等转移：beq）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
5. 考虑beq指令（条件转移指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 37: 分支指令的RTL描述
beq rs, rt, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Cond ← R[rs] - R[rt] 做减法比较rs和rt中的内容
  if (Cond eq 0) 计算下地址（根据比较结果，修改PC）
    PC ← PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC ← PC + 4
思考：立即数的含义是什么？是相对偏移指令条数还是存储单元数？
应在原数据通路上加哪些元件和连线？用什么控制信号来控制？
立即数用补码表示
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: How does the branch on equal instruction work?
Well it calculates the branch condition by subtracting the register selected by the Rt field from the register selected by the Rs field.
If the result of the subtraction is zero, then these two registers are equal and we take a branch. Otherwise, we keep going down the sequential path (PC <- PC +4).
+1 = 65 min. (Y:45)

## Slide 38: 条件转移指令的数据通路
beq rs, rt, imm16 We need to compare Rs and Rt !
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
ALU
PC
Clk
Next Addr
Logic
16
imm16
Branch
To Instruction
Memory
Zero
思考：下址逻辑如何设计？
RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg, Branch 各取何值？
0
1
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
x
0
subu
x
0
0
x
1
溢出
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let’s take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 39: 下地址计算逻辑的设计
PC是一个32位地址:
  顺序执行时: PC<31:0> = PC<31:0> + 4
  转移执行时: PC<31:0> = PC<31:0> + 4 + SignExt[imm16] X 4
MIPS是按字节编址，每条指令为32位，占4个字节，故PC的值总是4的倍数，即后两位为00，去除这2位，PC只需要30位即可。
下地址计算逻辑简化为：
顺序执行时: PC<31:2> = PC<31:2> + 1
  转移执行时: PC<31:2> = PC<31:2> + 1 + SignExt[imm16]
PC采用30位后，其转移地址计算逻辑变得更加简单。
实现时需要做两次加法，用两个加法器完成，“X4”操作用左移2位实现。
扩展成30位
取指令时: 指令地址 = PC<31:2> 串接 “00”
为了简化运算可以采用以下措施：
Notes: In theory, the Program Counter (PC) is a 32-bit byte address into the Instruction memory.
The Program Counter is increment by four after each sequential instruction.
When a branch is taken, we need to sign extend the 16 bit immediate field, multiply this sign extended value by four, and add it to the sequential instruction address (PC + 4).
Why does this magic number “4” always come up? Well the reason is that the 32-bit PC is a byte address and all MIPS instructions are four bytes, or 32 bits, long.
In other words, if we keep a 32-bit Program Counter, then the two least significant bits of the Program Counter will always be zeros.
And if these two bits are always zeros, there is no reason to have hardware to keep them.
So in practice, we will simply the hardware by using a 30 bit program counter.
That is, we will build a Program Counter that only keep tracks of the upper 30 bits (<31:2>) of the instruction address because we know the 2 least significant bits will always be 0s.
Then instead of always increase the Program Counter by four for sequential operation, we only have to increase it by 1.
And for branch operation, we don’t need to multiply the sign extended immediate field by four before adding to the sequential PC (PC + 1).
And when we apply the program counter to the address of the instruction memory, we need to attach two zeros to its least significant bits.
+3 = 70 min. (Y:50)

## Slide 40: 下地址逻辑设计
用30-bit PC:
  顺序执行时: PC<31:2> = PC<31:2> + 1
  转移执行时: PC<31:2> = PC<31:2> + 1 + SignExt[imm16]
  取指令时: 指令地址 = PC<31:2> 串接 “00”
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch
Zero
Addr<31:2>
Instruction
Memory
Addr<1:0>
“00”
32
Instruction<31:0>
Instruction<15:0>
30
先根据当前PC取指令， 计算的下条指令地址在下一个时钟到来后才能写入PC！
标志位ZF，由ALU产生！
为什么这里没有用“ALU”而是用“Adder”? “ALU”和“Adder”有什么差别？
Notes: So let’s see how we can put all these theories (point to the equations) into practice.
The PC plus one is implemented by this first adder here.
For branch operation, we need to sign extend the immediate field of the instruction and then add it to the output of the first adder to implement this equation (PC + 1 + SignExt(imm16)).
For sequential operation, the output of the first adder is selected by the two-to-one mux so it will be saved into the PC register at the next clock tick.
For a taken branch, that is we have a branch_on_equal and the condition Zero is true, the output of the second adder is selected.
In all cases, the 30 bit Program Counter is used as instruction address bit 31 to bit 2.
The two least significant bits of the instruction address will always be zeroes.
One question you may want to ask is: Do we really need an adder just to add “1”?
Well may be not.
+2 = 72 min. (Y:52)

## Slide 41: 无条件转移指令
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
6. 考虑Jump指令（无条件转移指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 42: 无条件转移指令的RTL描述
j target
  M[PC] 取指令（公共操作，取指部件完成）
  PC<31:2> ← PC<31:28> 串接 target<25:0> 计算目标地址
思考：应在原数据通路上加哪些元件和连线？用什么控制信号来控制？
想一想：跳转指令的转移范围有多大？
是当前指令后面的0x000 0000~0xFFF FFFC 处？
不是！它不是相对寻址，是绝对寻址。转移范围只能在j指令所在的228=256MB页面内，页面号与j指令相同PC<31:28>
FFFF FFFF
F000 0000
EFFF FFFF
E000 0000
AFFF FFFF
A000 0000
0FFF FFFF
0000 0000
j target
op
target address
0
26
31
6 bits
26 bits
j target所在页号
Notes: Finally, let’s take a look at the jump instruction which uses the J format.
The effect of the jump instruction is to change the lower 26 bits of the Program Counter to the value specified in the address field of the instruction.
+1 = 76 min. (Y:46)

## Slide 43: Instruction Fetch Unit: 取指令部件
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch
Zero
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
j target
  PC<31:2> ← PC<31:28> concat target<25:0>
Instruction<15:0>
Instruction<31:0>
imm16、Target、…
30
26
4
Mux
1
0
Target
30
Jump
Instruc<25:0>
这是“取指部件”的完整设计
3 个输入: Jump, Branch, Zero
1个输出: 指令字
PC的改变在下个Clk到达后发生！
RegDst, ALUctr, ExtOp, ALUSrc, MemtoReg, RegWr, MemWr, Branch, Jump 取值？
X
0
0
x
1
PC<31:28>
PC<31:2>
Notes: Well this (points to the equation) is easy to implement.
All we have to do is grab the four most significant bits of the PC and put them right next to the 26 bits target, and we will have the next PC for the jump (point to the feedback path).
If we are running Powerview, what we will do now is to create a symbol called Instruction Fetch Unit.
The output of this symbol is the 32-bit instruction word.
The input to the Instruction Fetch Unit are two control signals, Branch and Jump, and one conditional input Zero from the datapath.
Using this new symbol, we can complete our single cycle datapath.
+2 = 78 min. (Y:58)

## Slide 44: 实现7条MIPS指令的单周期处理器的数据通路
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32 bit
Registers
rs
rt
rt
rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump
Branch
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
指令执行结果总是在下个时钟到来的开始保存在 寄存器 或 存储器 或 PC 中！
下一讲介绍：如何产生控制信号！（控制器的设计内容）
溢出
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them in the next class..
+2 = 80 min. (Z:00)

## Slide 45: 数据通路中的关键路径(Load操作)花费的时间
记住：寄存器组和理想存储器的定时方式
  写操作时，作为时序逻辑电路。即：
    时钟到达前，输入需“建立时间(setup time)”；到达后经“Clk-to-Q”时间后写入数据到达输出端。
  读操作时，作为组合逻辑电路。即：
    地址有效后经过“取数时间(access time)”，输出开始有效.
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
rd
ALU
Clk
DataIn
DataOut
Data
Address
Ideal
Data
Memory
Instruction bus
Instruction Address
Ideal
Instruction
Memory
Clk
PC
5
rs
5
rt
16
imm16
32
32
32
32
Load操作：
R[rt] ← M[R[rs]+imm16]
关键路径时长 = PC的 Clk-to-Q时间 +
指令存储器的取数时间 +
寄存器组的取数时间+
ALU 加法延时+
数据存储器的取数时间+
写寄存器的建立时间+
时钟偏移
Ext
这就是Clk的周期！
Notes: Now with the clocking methodology back in your mind, we can think about how the critical path of our “abstract” datapath may look like.
One thing to keep in mind about the Register File and Ideal Memory (points to both Instruction and Data) is that the Clock input is a factor ONLY during the write operation.
For read operation, the CLK input is not a factor. The register file and the ideal memory behave as if they are combinational logic.
That is you apply an address to the input, then after certain delay, which we called access time, the output is valid.
We will come back to these points (point to the “behave” bullets) later in this lecture.
But for now, let’s look at this “abstract” datapath’s critical path which occurs when the datapath tries to execute the Load instruction.
The time it takes to execute the load instruction are the sum of:
(a) The PC’s clock-to-Q time.
(b) The instruction memory access time.
(c) The time it takes to read the register file.
(d) The ALU delay in calculating the Data Memory Address.
(e) The time it takes to read the Data Memory.
(f) And finally, the setup time for the register file and clock skew.
+3 = 21 (Y:01)
Complement:
Clock skew(B-40):

## Slide 46: 数据通路设计小结
MIPS指令集的一个子集作为CPU的实现目标
  公共操作：取指令和PC+4
  下址计算：30位PC，三路选择：顺序、Branch（结合标志Zero）、Jump
  R型数据通路：ALU两个操作数来自rs和rt，结果写到rd
  访存数据通路：符号扩展，数据在rt和主存单元中交换
  立即数ori数据通路：0扩展后的操作数送到ALU的一个输入端

## Slide 47: 控制器在计算机组成结构中的位置
控制器在计算机的五大部件中的位置
Control
Datapath
Memory
Processor
Input
Output
下一个目标：设计单周期数据通路的控制器。
设计方法：
根据每条指令的功能，分析控制信号的取值，并列表表示。
根据列出的指令和控制信号的关系，写出每个控制信号的逻辑表达式。
Notes: So where are in in the overall scheme of things.
Well, we just finished designing the processor’s datapath.
Now I am going to show you how to design the control for the datapath.
+1 = 7 min. (X:47)

## Slide 48: Add / Sub操作开始时取指部件中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Adder
30
30
Branch = 旧值
Zero = 旧值
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
取指令: Instruction ← M[PC]
  所有指令都相同
Jump = 旧值
Instruction<15:0>
Instruction<31:0>
30
Instr<25:0>
Clk
新指令还没有取出译码，所以控制信号的值还是原来指令的旧值。
新指令还没有执行，所以标志也为旧值。
取出指令的第31-26位作为操作码首先被译码。op=000000, 则为R-type指令
取指部件由旧控制信号控制，会不会有问题？
没有问题！Why?
因为在下个Clk到来之前PC输入端的值不会写入，只要保证下个Clk来之前能产生正确的PC即可！
Notes: First let’s look at the Instruction Fetch Unit where everything begins.
Every instruction begins at the clock tick. The clock tick in this case is the high to low transition of the Clk (points to the “bubble” of PC).
What happens right after the clock tick?
After Clk-to-Q delay, the PC gets the value that points to the Add instruction and fetch the add instruction from the memory but sending the address to the Ideal Instruction memory.
Notice that since this is the beginning of the instruction, Control signals Branch and Jump will still have the old values from the previous instruction.
At the beginning of ALL instructions execution, the instruction unit behaves the same way as shown here and we won’t repeat this picture for every instruction.
+2 = 12 min. (X:52)

## Slide 49: 指令译码后R型指令（Add / Sub）操作过程
32
ALUctr = Add or Sub
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = 1
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rd] ← R[rs] + / - R[rt]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.
+3 = 15 min. (X:55)

## Slide 50: R型指令（Add /Sub）最后阶段取指部件中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC + 4
  7条指令中除 beq 和 J指令以外的指令都相同
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
因为新的控制信号保证了正确的PC值的产生，在足够长的时间后，下个时钟Clk下降沿到来时将其值打入PC！
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch and Jump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 51: Register-Register（R型指令） 时序
Clk
PC
rs, rt, rd,
Op, Func
Clk-to-Q
ALUctr
指令存储器取数时间
Old Value
New Value
RegWr
Old Value
New Value
控制单元延迟
busA, B
寄存器组取数时间
Old Value
New Value
busW
ALU 延迟
Old Value
New Value
Old Value
New Value
New Value
Old Value
写入寄存器
PC+4
PC+4 PC
PC建立时间
rd建立时间
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time(虽然早就产生，但PC值的改变一定在时钟边沿的控制下进行的).
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)
Complement:
Instruction bus: see slide 12 on An Abstract View of the Critical Path

## Slide 52: ori 指令译码后的执行过程
32
ALUctr = or
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 0
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rt] ← R[rs] or ZeroExt[Imm16]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
op
rs
rt
immediate
0
16
21
26
31
Notes: Now let’s look at the control signals setting for the Or immediate instruction.
The OR immediate instruction OR the content of the register specified by the Rs field to the Zero Extended Immediate field and write the result to the register specified in Rt.
This is how it works in the datapath. The Rs field is fed to the Ra address port to cause the contents of register Rs to be placed on busA.
The other operand for the ALU will come from the immediate field. In order to do this, the controller need to set ExtOp to 0 to instruct the extender to perform a Zero Extend operation.
Furthermore, ALUSrc must set to 1 such that the MUX will block off bus B from the register file and send the zero extended version of the immediate field to the ALU.
Of course, the ALUctr has to be set to OR so the ALU can perform an OR operation.
The rest of the control signals (MemWr, MemtoReg, Branch, and Jump) are the same as theAdd and Subtract instructions.
One big difference is the RegDst signal. In this case, the destination register is specified by the instruction’s Rt field, NOT the Rd field because we do not have a Rd field here.
Consequently, RegDst must be set to 0 to place Rt onto the Register File’s Rw address port.
Finally, in order to accomplish the register write, RegWr must be set to 1.
+3 = 20 min. (X:60)

## Slide 53: Load指令译码后的执行过程
32
ALUctr = addu
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = 1
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
Rd
Rt
Rs
R[rt] ← Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31
ALUtcr应为add还是addu？差别在于溢出标志！
Overflow
=0
Notes: Let’s continue our lecture with the load instruction. What does the load instruction do?
It first adds the contents of the register specified by the Rs field to the Sign Extended version of the Immediate field to form the memory address.
Then it uses this memory address to access the memory and write the data back to the register specified by the Rt field of the instruction.
Here is how the datapath works: first the Rs field is fed to the Register File’s Ra address port to place the register onto bus A.
Then the ExtOp signal is set to 1 so that the immediate field is Sign Extended and we place this value (output of Extender) onto the ALU input by setting ALUsrc to 1.
The ALU then add (ALUctr = add) the two together to form the memory address which is then placed onto the Data Memory’s address port.
In order to place the Data Memory’s output bus onto the Register File’s input bus (busW), the control needs to set MemtoReg to 1.
Similar to the OR immediate instruction I showed you earlier, the destination register here is specified by the Rt field. Therefore RegDst must be set to 0.
Finally, RegWr must be set to 1 to complete the register write operation.
Well, it should be obvious to you guys by now that we need to set Branch and Jump to 0 to make sure the Instruction Fetch Unit update the Program Counter correctly.
+3 = 28 min. (Y:08)

## Slide 54: sw指令译码后的执行过程
32
ALUctr = addu
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 1
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
M{R[rs] + SignExt[imm16]} ← R[rt]
op
rs
rt
immediate
0
16
21
26
31
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)

## Slide 55: beq指令译码后条件码的产生过程
32
ALUctr = subu
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 1
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
Rd
Rt
Rs
if (R[rs] - R[rt] == 0) then Zero ← 1 ; else Zero ← 0
op
rs
rt
immediate
0
16
21
26
31
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 56: beq指令最后阶段取指部件中的动作
if (Zero == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 1
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
Zero = 1
若beq指令执行使Zero=0，信息又是如何流动的？
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the sequential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 57: Jump指令译码后的执行过程
32
ALUctr = x
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = x
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 1
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rt
rs
IFU中目标地址送PC，其他什么都不做（只要保证存储部件不发生写的动作）
op
target address
0
26
31
如何保证存储部件不发生写？
使相应的写使能信号为0！
Notes: The control signals setting in the main datapath for the Jump instruction is pretty boring because in most cases, we DON’T CARE.
More specifically, control signals ExtOp, ALUSrc, ALUctr are all don’t cares because the ALU is not used at all for the Jump instruction.
Control signals MemtoReg and RegDst are don’t are because Jump does not write the register file. That is the reason why we still need to set RegWr to zero.
Furthermore, we also need to set MemWr to zero to avoid Data Memroy write.
Finally, the control signal Branch is set to zero but Jump is set to 1.
+2 = 37 min. (X:17)
Complement: So far as we have already seen, almost all instructions use ALU. But this jump instruction is exceptional.
which instruction doesn't use ALU?

## Slide 58: Jump指令结束前IFU中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC<31:28> concat target<25:0> concat “00”
Jump = 1
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
op
target address
0
26
31
后条件码的产生
Notes: Inside the Instruction Fetch Unit, with Branch set to zero and Jump set to 1, we will not use the output of neither Adder.
What we will use is the concatenation of the four most significant bits of the current program counter and the twenty six bits of the target address.
With the control signal Jump set to 1, this value will be send to the Program Counter and get written into PC at the next clock tick (points to the Clk bubble).
+2 = 39 min. (Y:19)
There should be an improvement: When Jump=1, we don’t have to set Branch=0. We can set Branch=x to simply logical design of the control part. But we have to set Jump=0 when Branch=1.

## Slide 59
ALU的控制设计-实现7条MIPS指令的ALU
实现7条指令的ALU运算功能如下表所示：
ori
lw
sw
beq
jump
运算
or
addu
addu
subu
x
指令
add
sub
sub
add
add：有溢出判断的加法
sub：有溢出判断的减法
addu：无溢出判断的加法，即加法器的溢出标志位不输出(Overflow=0)。
subu：无溢出判断的减法，即加法器的溢出标志位不输出(Overflow=0)。
or：按位逻辑或运算
ALU中最核心的是加法器，加上各种逻辑电路可实现减法、无溢出判断的加减法、逻辑运算or等运算操作。
5种不同的运算功能，需要3位选择信号ALUctr[2:0] 。通过输入不同的ALUctr产生相应的逻辑电路控制信号，让加法器和外围逻辑电路实现指定的运算功能。
010
011
100
101
运算
or
未用
subu
sub
ALUctr[2:0]
000
001
addu
add
110 111
未用
ALUctr三位控制信号组合与对应的运算功能：

## Slide 60: 综合分析结果，得到指令与控制信号的关系表
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
add
1
0
0
1
0
0
0
x
sub
0
1
0
1
0
0
0
0
or
0
1
1
1
0
0
0
1
addu
x
1
x
0
1
0
0
1
addu
x
0
x
0
0
1
0
x
subu
x
x
x
0
0
0
1
x
xxx
op
target address
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
10 0000
10 0010
与func字段无关！
指令
控制信号
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something called “local decoding.”
+3 = 42 min. (Y:22)

## Slide 61: 控制器分为：主控制单元和ALU局部控制单元
MIPS指令格式中指示操作性质有op 和 func两个字段，分别用来产生两类不同的控制信号
func只用于R型指令，形成对应的ALU的功能控制信号。
op用来产生各种控制信号，包括了非R型指令的ALU功能控制信号。
ALUctr的值：
对于非R型指令，等于ALUop;
对于R型指令，由func译码产生。
3
ALU
func
Main
Control
op
6
ALU
Control
(Local)
N=?
6
ALUop
ALUctr
R-Type
0
1
3
控制器 = 主控制单元 + ALU局部控制单元
ALUctr有5种操作，需3位，ALUop应与其长度一致，故N为3！
Notes: That is, instead of asking the Main Control to generates the ALUctr signals directly (see the diagram with the ALU), the main control will generate a set of signals called ALUop.
For all I and J type instructions, ALUop will tell the ALU Control exactly what the ALU needs to do (Add, Subtract, ...) .
But whenever the Main Control sees a R-type instructions, it simply throws its hands up and say: “Wow, I don’t know what the ALU has to do but I know it is a R-type instruction” and let the Local Control Block, ALU Control to take care of the rest.
Notice that this save us one column from the table we had on the last slide. But let’s be honest, if one column is the ONLY thing we save, we probably will not do it.
But when you have to design for the entire MIPS instruction set, this column will used for ALL R-type instructions, which is more than just Add and Subtract I showed you here.
Another advantage of this table over the last one, besides being smaller, is that we can uniquely identify each column by looking at the Op field only.
Therefore, as I will show you later, the Main Control ONLY needs to look at the Opcode field.
How many bits do we need for ALUop?
+3 = 45 min. (Y:25)

## Slide 62: 主控单元输出信号ALUop的逻辑表达式
ALUop的编码定义如下：
ALUop是用于非R型指令产生ALUctr，因此与R型指令无关。
Jump指令的执行不使用ALU，故与ALUop无关。
R型指令所需ALUctr与func有关，它们在局部控制器中产生。
func
Main
Control
op
6
ALU
Control
(Local)
3
6
ALUop
ALUctr
R-Type
0
1
R-type
ori
lw
sw
beq
jump
运算
由func指定
or
addu
addu
subu
x
ALUop<2:0>
xxx
010
000
000
100
xxx
指令
ALUop<0>=0
ALUop<1>=ori
ALUop<2>=beq
3
3
Notes: What this table and diagram implies is that if the ALU Control receives ALUop = 100, it has to decode the instruction’s “func” field to figure out what the ALU needs to do.
Based on the MIPS encoding in Appendix A of your text book, we know we have a Add instruction if the func field is 10 000.
If the func field is 10 0010, we know we have a subtract operation and so on.
Notice that the bit 5 and bit 4 of this field is the same for all these operations so as far as the ALU control is concerned, these bits are don’t care.
Now recall from your ALU homework, the ALUctr signals has the following meaning (point to the table): 000 means Add, 001 means subtract, ... etc.
Based on these three tables (point to the last row of the top table and then the two other tables) and the fact that bit 5 and bit 4 of the “func” field are don’t care, we can derive the following truth table for ALUctr.
+2 = 48 min. (Y:28)

## Slide 63: ALU局部控制器输出信号的逻辑表达式
ALUctr<0> = 1
ALU
func<5:0>
指令
10 0000
10 0010
add
sub
ALUctr<2:0>
ALU Operation
001
101
add
sub
ALUctr<1> = 0
ALUctr<2> = func<1>
func
Main
Control
op
6
ALU
Control
(Local)
6
ALUop
ALUctr
R-Type
0
1
000000
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
R-type
由于7条指令系统中只有add和sub两条R型指令，局部控制器逻辑就很简单
3
3
3
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 by collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the product terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don’t care term.
With all these don’t care terms, the logic equation is rather simple.
The first product term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don’t care becomes ...
+2 = 57 min. (Y:37)

## Slide 64: 主控制单元的真值表
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALU运算控制
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Addu
x
1
x
0
1
0
0
1
Addu
x
0
x
0
0
1
0
x
Subu
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
ALUop <2>
x
0
0
0
1
x
ALUop <1>
x
1
0
0
0
x
ALUop <0>
x
0
0
0
0
x
Main
Control
op
6
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
RegDst
ALUSrc
:
主控单元的输入
主控单元的输出
R-type
1
0
0
0
0
0
R-Type
1
0
Notes: Now that we have taken care of the Local Control (ALU Control), let’s refocus our attention to the Mian Controller.
The job of the Main Control is to look at the Opcode field of the instruction and generate these control signals for the datapath (RegDst, ... ExtOp) as well as the 3-bit ALUop field for the ALU Control.
Here, I have shown you the symbolic value of the ALUop field as well as the actual bit assignment.
For example here (2nd column), the R-type ALUop is encode as 100 and the Add operation (3rd column) is encoded as 000..
This is call a quote “Truth Table” unquote because if you think about it, this is like having the truth table rotates 90 degrees.
Let me show you what I mean by that.
+3 = 65 min. (Y:45)

## Slide 65: 考察每个控制信号的逻辑方程（如：RegWrite）
R-type
ori
lw
sw
beq
jump
RegWrite
1
1
1
0
0
0
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
RegWrite = R-type + ori + lw
  = !op<5> & !op<4> & !op<3> & !op<2> & !op<1> & !op<0> (R-type)
  + !op<5> & !op<4> & op<3> & op<2> & !op<1> & op<0> (ori)
  + op<5> & !op<4> & !op<3> & !op<2> & op<1> & op<0> (lw)
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
指令译码器
Notes: For example, consider the control signal RegWrite.
If we treat all the don’t cares as zeros, this row here means RegDest has to be equal to one whenever we have a R-type, or an OR immediate, or a load instruction.
Since we can determine whether we have any of these instructions (point to the column headers) by looking at the bits in the “OP” field, we can transform this symbolic equation to this binary logic equation.
For example, the first product term here say we have a R-type instruction whenever all the bits in the “OP” field are zeros.
So each of these big AND gates implements one of the columns (R-type, ori, ...) in our table. Or in more technical terms, each AND gate implements a product term.
In order to finish implementing this logic equation, we have to OR the proper terms together.
In the case of the RegWrite signal, we need to OR the R-type, ORi, and load terms together.
+2 = 67 min. (Y:47)

## Slide 66: Main Control的PLA实现
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
ALUop<0>
ALUop<1>
ALUop<2>
指令译码器
‘0’
R-Type
Notes: Similarly, for ALUSrc, we need to OR the ori, load, and store terms together because we need to assert the ALUSrc signals whenever we have the Ori, load, or store instructions.
The RegDst, MemtoReg, MemWrite, Branch, and Jump signals are very simple. They don’t need to OR any product terms together because each is asserted for only one instruction.
For example, RegDst is asserted ONLY for R-type instruction and MemtoReg is asserted ONLY for load instruction.
ExtOp, on the other hand, needs to be set to 1 for both the load and store instructions so the immediate field is sign extended properly.
Therefore, we need to OR the load and store terms together to form the signal ExtOp.
Finally, we have the ALUop signals.
But clever encoding of the ALUop field, we are able to keep them simple so that no OR gates is needed.
If you don’t already know, this regular structure with an array of AND gates followed by another array of OR gates is called a Programmable Logic Array, or PLA for short.
It is one of the most common ways to implement logic function and there are a lot of CAD tools available to simplify them.
+3 = 70 min. (Y:50)

## Slide 67
<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
指令译码器
op<5>
.
.
<0>
bne
Notes: Similarly, for ALUSrc, we need to OR the ori, load, and store terms together because we need to assert the ALUSrc signals whenever we have the Ori, load, or store instructions.
The RegDst, MemtoReg, MemWrite, Branch, and Jump signals are very simple. They don’t need to OR any product terms together because each is asserted for only one instruction.
For example, RegDst is asserted ONLY for R-type instruction and MemtoReg is asserted ONLY for load instruction.
ExtOp, on the other hand, needs to be set to 1 for both the load and store instructions so the immediate field is sign extended properly.
Therefore, we need to OR the load and store terms together to form the signal ExtOp.
Finally, we have the ALUop signals.
But clever encoding of the ALUop field, we are able to keep them simple so that no OR gates is needed.
If you don’t already know, this regular structure with an array of AND gates followed by another array of OR gates is called a Programmable Logic Array, or PLA for short.
It is one of the most common ways to implement logic function and there are a lot of CAD tools available to simplify them.
+3 = 70 min. (Y:50)

## Slide 68
控制器设计小结
1. 控制器设计的关键是找出指令格式中规定指令功能（类型）的字段与各条指令所需要的控制信号之间的关系。
MIPS指令中有op和func两个字段用来表示指令的功能。
(1)R型指令：所有指令的op字段都为000000，各指令的func字段用来产生ALU的控制信号，决定执行的操作（加、减、逻辑与…），其它数据通路的控制信号各指令都相同（仅考虑三寄存器操作数）。
(2)其他类型指令：没有func字段，各指令的op字段不同，它产生包括ALU的所有数据通路的控制信号。
2. 控制器结构分成主控制器和ALU局部控制器两部分。
(1)ALU局部控制器是为R型指令产生ALU的控制信号，其输入为func字段；
(2)主控制器产生非R型指令的所有控制信号，以及R型指令的除ALU控制信号外的其他控制信号，其输入为op字段；
(3)将主控制器产生的ALU控制信号与ALU局部控制器的输出信号通过一个多路选择器合并后作为最终的ALU控制信号。多路选择器的选择信号(R-Type)由主控制器产生。

## Slide 69: 执行前述7条指令的完整的单周期处理器
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rt
rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump
Branch
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
imm16
rd
rs
rt
Main
Control
op
6
ALU
Control
func
6
3
ALUop
ALUctr
3
RegDst
ALUSrc
:
Instr<5:0>
Instr<31:26>
Instr<15:0>
Overflow
R-Type
Notes: OK, now that we have the Main Control implemented, we have everything we needed for the single cycle processor and here it is.
The Instruction Fetch Unit gives us the instruction. The OP field is fed to the Main Control for decode and the Func field is fed to the ALU Control for local decoding.
The Rt, Rs, Rd, and Imm16 fields of the instruction are fed to the data path.
Based on the OP field of the instruction, the Main Control will set the control signals RegDst, ALUSrc, .... etc properly as I showed you earlier using separate slides.
Furthermore, the ALUctr use the ALUop from the Main control and the func field of the instruction to generate the ALUctr signals to ask the ALU to do the right thing: Add, Subtract, Or, and so on.
This processor will execute each of the MIPS instruction in the subset in one cycle.
There is, however, a couple of subtle differences between this single-cycle processor and a real MIPS processor in terms of instruction execution.
+2 = 72 min (Y:52)

## Slide 70: lw指令的执行时间最长, 它所花时间作为时钟周期
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA
Register File Access Time
Old Value
New Value
busB
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
ExtOp
Old Value
New Value
ALUSrc
Old Value
New Value
MemtoReg
Old Value
New Value
Address
Old Value
New Value
busW
Old Value
New
Delay through Extender & Mux
Register
Write Occurs
Data Memory Access Time
PC+4
建立时间
Notes: This timing diagram shows the worst case timing of our single cycle datapath which occurs at the load instruction.
Clock to Q time after the clock tick, PC will present its new value to the Instruction memory.
After a delay of instruction access time, the instruction bus (Rs, Rt, ...) becomes valid.
Then three things happens in parallel:
(a) First the Control generates the control signals (Delay through Control Logic).
(b) Secondly, the register file access is to put Rs onto busA.
(c) And we have to sign extended the immediate field to get the second operand (busB).
Here I assume register file access takes longer time than doing the sign extension so we have to wait until busA valid before the ALU can start the address calculation (ALU delay).
With the address ready, we access the data memory and after a delay of the Data Memory Access time, busW will be valid.
And by this time, the control unit would have set the RegWr signal to one so at the next clock tick, we will write the new data coming from memory (busW) into the register file.
+3 = 77 min. (Y:57)

## Slide 71: 单周期计算机的性能
单周期处理器的CPI为多少？
  其他条件一定的情况下，CPI越小，则性能越好！
单周期处理器的性能会不会很好？为什么？
  计算机的性能除CPI外，还取决于时钟周期的宽度。
  单周期处理器的时钟宽度为最复杂指令的执行时间。
  很多指令可以在更短的时间内完成，但都花了同样的时间。
CPI=1!

## Slide 72: 单周期计算机的性能分析例子
假设在单周期处理器中，各主要功能单元的操作时间为：
存储单元：200ps
ALU和加法器：100ps
寄存器堆（读/写）：50ps
假设MUX、控制单元、PC、扩展器和传输线路都没有延迟，则下面实现方式中，哪个更快？快多少？
（1）每条指令在一个固定长度的时钟周期内完成
（2）每条指令在一个时钟周期内完成，但时钟宽度按指令所需调整，也即为可变的（实际不可行，只是为了比较）
假设程序中各类指令占比：25%取数、10%存数、45%ALU、15%分支、5%跳转

## Slide 73: 单周期计算机的性能
解：CPU执行时间=指令条数 x CPI x 时钟周期=指令条数 x 时钟周期
两种方案的指令条数都一样，CPI都为1，所以只要比较时钟周期宽度即可。
各类指令要求的时间长度为：

## Slide 74: 单周期计算机的性能
对于方式（1），时钟周期由最长指令来决定，应该是load指令，为600ps
对于方式（2），时钟周期取各条指令所需时间，时钟周期从600ps至200ps
根据各类指令的频度，计算出平均时钟周期长度为：
CPU时钟周期=600x25%+550x10%+400x45%+350x15%+200x5%=447.5ps
由此可见，可变时钟周期的性能是定长周期的1.34倍！
但是，对每类指令采用可变长时钟周期实现非常困难，而且所带来的额外开销会很大，不合算！
多周期数据通路和控制器就是用于解决上述问题的方案，其特点是：
时钟周期固定、时钟周期数可变
早期的小指令集计算机用过单周期实现技术，但现代计算机都不采用。
方式(1)的CPU执行时间
方式(2)的CPU执行时间
方式(1)的CPU 时钟周期
方式(2)的CPU 时钟周期
600
447.5
CPU性能比=
=
=
= 1.34

## Slide 75: 第二讲 小结
考察每条指令在单周期数据通路中的执行过程
  每条指令在一个时钟周期内完成
  每个时钟到来时，都开始进入取指令操作
    经过clk-to-Q，PC得到新值，经过access time后得到当前指令
    按三种方式分别计算下条指令地址，在branch / zero / jump的控制下，选择其中之一送到PC输入端，但不会马上写到PC中，一直到下个时钟到达时，才会更新PC。三种下址方式为：
      branch=jump=0：PC+4
      branch=zero=1： PC+4+signExt[imm16]*4
      jump=1： PC<31:28> concat target<25:0> concat “00”
  指令取出后被译码，产生指令对应的控制信号
    R-type指令：rd为目的寄存器，无访存操作，……
    ori指令：rt为目的寄存器，0扩展，无访存操作，……
    lw指令： rt为目的寄存器，计算地址、符号扩展，读内存，……
    sw指令： rt为源寄存器，计算地址、符号扩展，写内存，……
汇总每条指令控制信号的取值，生成真值表，写出逻辑表达式，设计主控制逻辑和ALU局部控制逻辑

## Slide 76: 第三讲 微程序设计和异常处理
微程序设计
  硬连线控制器设计的优点和缺点
  微程序控制器的基本思想
  微程序、微指令、微操作和微命令的概念及其关系
  微指令格式设计
CPU对异常的处理
  “异常”和“中断”的概念
  如何在数据通路中加入异常处理部件
  如何控制数据通路中的异常处理部件
主 要 内 容

## Slide 77: 硬连线控制器和微程序控制器
硬连线控制器的特点
优点：速度快，适合于简单或规整的指令系统，例如，MIPS指令集。
缺点：它是一个多输入/多输出的巨大逻辑网络。对于复杂指令系统来说，结构庞杂，实现困难；修改、维护不易；灵活性差。
简化控制器设计的一个方法：微程序设计
微程序控制器的基本思想
  仿照程序设计的方法，编制每条指令对应的微程序
  每个微程序由若干条微指令构成，一条微指令包含若干个微命令
  所有指令对应的微程序放在只读存储器中，执行某条指令就是取出对应微程序中的各条微指令，对微指令译码产生对应的微命令(即控制信号)。
  这个只读存储器称为控制存储器（Control Storage），简称控存CS 。
微程序设计的特点：具有规整性、可维护性和灵活性，但速度慢。

## Slide 78: 微程序控制器的基本结构
输入：指令、条件码
输出：控制信号(微命令)
核心：控存CS
µPC：指出将要执行的微指令在CS中的位置
µIR： 正在执行的微指令
每个时钟执行一条微指令
微程序第一条微指令地址由起始地址发生器产生
顺序执行时， µPC+1
转移执行时，由转移控制字段指出对哪些条件码进行测试，转移地址发生器根据条件码修改µPC
指令
早期把固化在ROM的微程序称固件（Firmware），表示用软件实现的硬部件，现在对固件通俗的理解是在ROM中“固化的软件”。

## Slide 79: 微程序\微指令\微命令\微操作的关系
一条机器指令
一个微程序
微指令1
微指令2
微指令n
微命令1
微命令2
微命令m
微操作
微操作
微操作
将指令的执行转换为微程序的执行
微程序是一个微指令序列
每条微指令是一个0/1序列，其中包含若干个微命令（即：控制信号）
微命令控制数据通路的执行
一般程序执行要解决什么问题？
(1) 指令如何译码、执行
(2) 下条指令到哪里去取
微程序执行也要解决两个问题：
(1)微指令如何对微命令编码
(2)下条微指令在哪里

## Slide 80: 第一个问题：微指令格式的设计
水平型微指令
基本思想：相容微命令尽量多地安排在一条微指令中。
优点：微程序短，并行性高，适合于较高速度的场合。
缺点：微指令长，编码空间利用率较低，并且编制困难。
垂直型微指令
基本思想：一条微指令只控制一、二个微命令。
优点：微指令短，编码效率高，格式与机器指令类似，故编制容易。
缺点：微程序长，一条微指令只能控制一、二个操作，无并行，速度慢

## Slide 81
微指令格式设计风格取决于微操作码的编码方式
µOP的编码方式有：
  不译法（直接控制法）
  字段直接编码（译）法
  字段间接编码（译）法
  最小（最短、垂直）编码（译）法
水平型微指令风格
垂直型微指令风格
微指令格式：
µOP
µAddr
微指令中包含了：若干微命令、下条微指令地址（可选）、常数（可选）
常数
µOP: 微操作码字段，产生微命令；
µAddr：微地址码字段，产生下条微指令地址。

## Slide 82: 第二个问题：下条微地址的确定方式
微程序执行顺序的控制问题
  在现行微指令执行完毕后，怎样控制产生下一条微指令的地址。
怎样控制微程序的执行顺序？
  通过在本条微指令中明显或隐含地指定下条微指令在控存中的地址来控制。
微指令地址的产生方法有两种：
  增量(计数器)法：下条微指令地址隐含在微程序计数器μPC中。
  断定(下址字段)法：在本条微指令中明显指定下条微指令地址。
选择下条要执行的微指令有以下四种情况：
  取指微程序首址：每条指令执行前，CPU先执行取指微程序。
  第一条微指令：每条指令取出后，必须转移到该指令对应的第一条微指令执行。
  顺序执行时：微程序执行过程中顺序取出下条微指令执行。
  分支执行时：在遇到按条件转移到不同微指令执行时，需要根据控制单元的输入来选择下条微指令。
问题：机器指令是隐含还是明显指出下条指令地址的？

## Slide 83: 异常和中断的处理
程序执行过程中CPU会遇到一些特殊情况，使正在执行的程序被“中断”
  此时，CPU中止原来正在执行的程序，转到处理异常情况或特殊事件的程序去执行，执行后再返回到原被中止的程序处（断点）继续执行。
程序执行被 “中断” 的事件有两类
  内部“异常”：
    按发生原因分为硬故障异常和程序性异常两类
    硬故障异常
    程序性异常
  外部“中断”：
  外部中断是一种I/O方式，所以有关外部中断的概念将在第8章介绍。
  在CPU内部发生的意外事件或特殊事件
  在CPU外部发生的特殊事件，通过向CPU发“中断请求”信号，请求CPU处理。
  如打印机缺纸、外设准备好、采样计时到、DMA传输结束等。
    如电源掉电、硬件线路故障等
执行某条指令时发生的“例外(Exception)”，如溢出、缺页、非法指令、除数为0、堆栈溢出等等。
Notes: 一种情况：上课时由于机器死机（PPT不能放）或屏幕保护（黑屏）等，使上课不能再正常继续下去----“内部异常”
另一种情况：上课时突然有紧急事情需要上课老师出去处理一下，回头继续上课----“外部中断”
打铃下课是“内部异常”还是“外部中断”？

## Slide 84: 异常和中断的处理(续)
内部“异常” 按处理方式又分为故障、自陷和终止三类
  故障(fault) ：执行指令引起的异常事件，如溢出、缺页、堆栈溢出、访问超时等。
  自陷(Trap) ：预先安排的事件，如单步跟踪、系统调用(执行访管指令)等。是一种自愿中断。
  终止(Abort) ：硬故障事件，此时机器将“终止”，调出中断服务程序来重启操作系统。
不同体系结构和教科书对“异常”和“中断”定义的内涵不同，在看参考资料时要注意！
  思考2：哪些故障补救后可继续执行，哪些只好终止当前进程？
  缺页、TLB缺失等：补救后可继续，回到发生故障的指令重新执行；
  溢出、除数为0、非法操作、内存保护错等：终止当前进程。
  思考1：自陷处理完成后回到哪条指令执行？
回到下条指令！
“断点”为发生故障指令的地址
“断点”为发生下条指令的地址
“断点”是什么？ 随便！

## Slide 85: 处理器中的异常处理机制
检测到异常时，处理器必须进行以下基本处理：
① 关中断（“中断/异常允许”状态位清0）：使处理器处于“禁止中断”状态，以防止新异常(或中断)破坏断点、程序状态和现场（现场指通用寄存器的值）。
② 保护断点和程序状态：将断点和程序状态保存到堆栈或特殊寄存器中。即：
  PC→堆栈 或 EPC（专门存放断点的寄存器）
  PSWR →堆栈 或 EPSWR （专门保存程序状态的寄存器）
  PSW（Program Status Word）：程序状态字，包括条件码、中断码、状态位等。
  PSWR（PSW寄存器）：用于存放程序状态字的寄存器。如，X86的FLAGS）。
③ 识别异常事件：有软件识别和硬件识别（向量中断方式）两种不同的方式。

## Slide 86: 处理器中的异常处理机制（续）
异常识别的两种方式：软件识别和硬件识别（向量中断方式）。
（1）软件识别（MIPS采用）
设置一个异常状态寄存器（MIPS中为Cause寄存器），用于记录异常原因。操作系统使用一个统一的异常处理程序，该程序按优先级顺序查询异常状态寄存器的各位，识别出异常事件。
（例如：MIPS中位于内核地址0x8000 0180处有一个专门的异常处理程序，用于检测异常的具体原因，然后转到内核中相应的异常处理程序段中进行具体的处理）
（2）硬件识别（向量中断）（80x86采用）
用专门的硬件查询电路按优先级顺序识别异常，得到“中断类型号”，根据此号，到中断向量表中读取对应的中断服务程序的入口地址。

## Slide 87: 本讲小结
硬连线控制器的优点是速度快，适合于简单规整指令集的数据通路；缺点是设计周期长、繁琐、不灵活、不易修改和增删指令
微程序控制器借用程序设计思想，将每条指令涉及到的命令（微程序）用只读存储器保存起来，执行到某条指令时，把这条指令对应的微程序按序取出，转换为控制信号。
优点：简化设计、灵活、易修改、易维护；缺点：速度慢。
异常会改变程序执行流程，所以处理器设计要考虑异常处理
在数据通路中加入异常处理必须考虑：
  保存断点和异常原因，并将控制转到异常处理程序首地址处

## Slide 88: 本章总结1
CPU的主要功能
  周而复始执行指令
  执行指令过程中，若发现异常情况，则转异常处理
  每个指令结束，查询有没有中断请求，有则响应中断
CPU的内部结构
  由数据通路(Datapath)和控制单元(Control unit)组成
    数据通路中包含组合逻辑单元和存储信息的状态单元
      组合逻辑单元用于对数据进行处理，如：加法器、运算器ALU、扩展器（0扩展或符号扩展）、多路选择器、以及状态单元的读操作线路等。
      状态单元包括触发器、寄存器、寄存器堆、数据/指令存储器等，用于对指令执行的中间状态或最终结果进行保存。
    控制单元对指令进行译码，与指令执行得到的条件码或当前机器的状态、时序信号（时钟）等组合，生成对数据通路进行控制的控制信号

## Slide 89: 本章总结2
CPU中的寄存器
  用户可见寄存器（用户可使用）
    通用寄存器：用来存放地址或数据，需在指令中明显给出
    专用寄存器：用来存放特定的地址或数据，无需在指令中明显给出
    数据寄存器：专用于保存数据，可以是通用或专用寄存器
    地址寄存器：专用于保存地址，可以是通用或专用寄存器。如：段指针、变址器、基址器、堆栈指针、栈帧指针等。
    标志(条件码)寄存器：部分可见。由CPU根据指令执行结果设定，只能以隐含方式读出其中若干位，用户程序（非内核程序）不能改变
  控制和状态寄存器（用户不可使用）
    程序计数器PC
    指令寄存器IR
    存储器地址寄存器MAR
    存储器缓冲(数据)寄存器 MBR / MDR
    程序状态字寄存器PSWR
    临时寄存器：用于存放指令执行过程中的临时信息
    其他寄存器：如，进程控制块指针、系统堆栈指针、页表指针等

## Slide 90: 本章总结3
指令执行过程
  取指、译码、取数、运算、存结果、查中断
  指令周期：取出并执行一条指令的时间，由若干个时钟周期组成
  时钟周期：CPU中用于信号同步的信号，是CPU最小的时间单位
数据通路的定时方式
  现代计算机都采用时钟信号进行定时
  一旦时钟有效信号到来，数据通路中的状态单元可以开始写入信息
  如果状态单元每个周期都更新信息，则无需加“写使能”控制信号，否则，需加“写使能”控制信号，以使必要时控制信息写入寄存器
数据通路中信息的流动过程
  每条指令在取指令阶段和指令译码阶段都一样
  每条指令的功能不同，故在数据通路中所经过的部件和路径可能不同
  数据在数据通路中的流动过程由控制信号确定
  控制信号由控制器根据指令代码来生成

## Slide 91: 本章总结4
单周期处理器的设计
  每条指令都在一个时钟周期内完成
  时钟周期以最长的Load指令所花时间为准
  无需加临时寄存器存放指令执行的中间结果
  在一个周期内同一个功能部件不能重复使用
  控制信号在整个指令执行过程中不变。
微程序控制方式
  每个时钟周期所包含的控制信号的值的组合看成是一个0/1序列，每个控制信号对应一个微命令，控制信号取不同的值，就发出不同的微命令
  若干微命令组合成一个微指令，每条指令所包含的动作就由若干条微指令来完成，每来一个时钟，执行一条微指令
  每条指令对应一个微程序，执行时，先找到对应的第一条微指令，然后按照特定的顺序取出后续的微指令执行
  实现的控制器称为微程序控制器
  存放微程序的只读存储器称为控制存储器，简称控存CS

## Slide 92
作业
教材P191 4、5、6、7、12题
补充题1
在课件介绍的7条指令基础上，增加I型指令bne（不等转移）和R型指令jr（寄存器跳转）两条指令后，画出取指部件的逻辑结构图。
补充题2
在单周期MIPS处理器的数据通路中，下表中各指令执行时所需要的控制信号的取值填入表中。
指令 | RegDst | ALUSrc | ALUctr | MemWr | ExtOP | RegWr | MemtoReg
addu $10,$11,$12 |  |  |  |  |  |  | 
addi $10, $15, AAH |  |  |  |  |  |  | 
sw $10, 100($11) |  |  |  |  |  |  | 
bne $10, $15, 1234H |  |  |  |  |  |  | 
addu $10, $11, $12 //R[rd] <= R[rs] + R[rt], 在ALU中执行不带溢出的加法addu。
addi $10, $15, AAH //R[rt] <= R[rs] + SignExt[Imm16], ALU执行具有溢出判断的加法add。